Attention！

The products before to be installed and used ,you must read this manual, and save it for next ！

Perform standard：(GB/T5837-2008 The forms and basic parameters of constant filling fluid coupling)

YOXⅡz  Series

constant filling fluid coupling

Instructions

Guangdong Zhongxing power Transmission Co.,Ltd

Publication date: 092009

.

Contents

1.	Preface	2

2.	Construction	3

3.	Functions and Operation Principle	4

4.	Performance Parameters	5

5.	Installation	10

6.	Operating Fluid	11

7.	Precautions	13

8.  Trouble Shooting	14

9.  Mechanical Thermal Switch  WBQ-II	15

10. Repair	17

11. Wear-out parts	17

12.  Spare Parts and Service	17

# Preface

This manual will help you to use our coupling in a safe, proper and economical way.

This manual shall always be read and used by every person before working on the coupling, it shall be available on the machine site for easy reference.

The coupling is manufactured to the state of art and approved safety regulations. Nevertheless, proper installation, maintenance and handling is indispensable for the coupling to provide best performance and service life as well as to safeguard the safety of operating personnel.

The coupling is designed to transmit power at rated values and under definite conditions. Incorrect use including incorrect installation or filling, use for other purpose or excessive power or speed etc., will cause damages to the coupling and other machines and may even endanger the safety of operating personnel. The manufacturer is not liable for any responsibility on all losses out of incorrect handling of the coupling.

This manual has been issued with utmost care. However, in case you need any further information, please contact

Guangdong Zhongxing Power Transmission Co., Ltd.

45 Hedi Road, Ducheng town, Yunan County 527100

Guangdong Province

P.R.China

Tel:  ( 0766 ) 7592180 , 7331005，7596083

Fax:  (0766 ) 7596216, 7597178

http://www.gdzxpt.com      e-mail: gdzxpt@163.com

Guangzhou Office: 	Telephone: ( 86 20 )86599392	 Fax: ( 86 20 ) 86599384

Beijing Office:		Telephone: ( 86 10 ) 84612061, 84639700

Shanghai Office:	Tele/Fax:  ( 86 21 ) 56062987

Zhengzhou Ofice:  Tele/Fax:  (86 371) 68989281

Shengyang Office:  Tele/Fax:  (86 24) 85860443

Chengdu Office: 	Tele/Fax:  (86 28) 84372518

Wuhan Offic:		Tele/Fax:	(86 27) 51157031

Jinan Office:		Tele/Fax:	(86 531) 85808072

# Construction

Fig.1  Construction of  YOXⅡZ

1. Holding Disc  2.Delay Chamber  3. Filler Plug

4.Pump Wheel  5. Hub  6. Turbo wheel   7.Shell

8.Shaft   9.Brake wheel  10. Flexible element  11. Fusible plug

# Functions and Operation Principle

  - Hydrodynamic couplings is one of the hydrodynamic element which transmitted the power by fluid energy. It belongs the soft transmission which the two shafts are connected by it. It can be used in different fields of national economy with its various functions:

(1) 	To protect the motor from over speed or stop.

- When the motor starts at overload, to reduce the startup time and the average current and improve the starting ability of squirrel motor.

- To lessen the shock & vibration during startup and prevent from overload, making the use life of motor longer.

(4)	To improve the power of electric net when equipping with squirrel motor 	at 	1.2 times of rated load.

- To balance the loads and lengthen the use life of motors and in multi-motor drive system.

- To save energy and reduce the of operation cost .

- Simple and reliable in structure. No mechanical worn and no need for special maintenance.

- Better reliability with brake wheel.

  - Operating Principle

The working chamber of Fluid Coupling is partially filled by an operating fluid ( usually 32# turbo oil). It can ensure the soft connection of drive machine and working machine. When the Pump Wheel is driven by the drive machine, the rotating wheel brings the fluid into rotation and thus converts the input mechanical energy into potential and kinetic energy of the fluid because of the centrifugal force. The rotating fluid then drives the Turbo Wheel into rotation and therefore converts the energy back into mechanical energy through the Turbo Wheel and Coupling Hub to the driven machine. The energy transmission from Pump wheel (drive ) to Turbo wheel (driven) is  realized. In case of Turbo Wheel Drive, the Turbo wheel is drive part and Pump wheel is drive part.

# Performance Parameters

4.1 Calculation of Torque and Power

The following formulae can be used to calculate the Transmitted Torque and Transmitted Power at different input speed nB

M = λB·γ·nB2·D5

N = 1/975·λB·γ·nB3·D5

where:   M  -  Transmitted Torque (kg.m)

γ  -  Density of fluid (for #20 turbine oilγ= 860kg/m3)

nB   -  Input speed (rpm)

λB  -  Performance Figure (min2/m). It can be taken 1.6×10-5

D  -  Effective Diameter of Wheel (m)

N  -  Transmitted Power (kw)

4.2  Determination of Filling Quantity

The filling quantity depends on

1. Input Torque

2. Input Speed

3. Slip at rated torque (Slip = 1 – efficiencyη)

4. Orientation of installation

User shall follow the recommended filling quantity when it is provided.

User may also obtain the filling volume from Fig. 3, but it can only be used as a guide for trial. And depending on the trial result, filling level shall be adjusted to meet actual power transmitted by:

- Increase filling quantity if transmitted torque is not enough or

- Reduce filling quantity if transmitted torque is too high

However, the filling quantity can never exceed the maximum value nor less then the minimum value shown in Table 1.

Filling Quantity:62.5%

Working Fluid: #32 Turbine oil,Density γ=830 kg/m3

Operating Temperature:70°C~80°C

Fig.2-1 Characteristic Curves for YOXⅡZ Couplings

Filling Quantity:70% and 50%

Working Fluid: #32 Turbine oil,Density γ=830 kg/m3

Operating Temperature:70°C~80°C

Fig.2-2Characteristic Curves for YOXⅡZ Couplings

Filling Quantity:80% and55%

Working Fluid: #32 Turbine oil,Density γ=830 kg/m3

Operating Temperature:70°C~80°C

Fig.2-3 Characteristic Curves for YOXⅡZ Couplings

此页贴图3“传递功率N与充油率qc关系曲线图”

Fig.3 Characteristic Curves for YOXⅡZ Couplings

# Installation

Fig.4 Installation of Coupling

# 1.Micrometer  2.Connection shaft  3.Brake wheel

The couplings are installed as Pump wheel drive (Fig. 4). With the brake wheel and connection disc removed, the motor and working machines are not needed to move.

Follow this sequence to install the coupling:

1) Check radial runout of shafts of motor and driven machine

- Fit suitable keys on the shafts of motor and driven machine, apply a suitable lubricant.

- Put the connection disc to motor shaft. Fix the brake wheel to reducer machine. Then lift the couplings (with connection shaft) between them. Align according to the marks. Make motor together with coupling interlocked with Brake wheel and check end clearance; gap between two teeth shall be within 2-4 mm.

- Slightly fasten bolts on the motor and reducer, check alignment of input shaft and output shaft with dial gauge, make sure that they fall within the following admissible values. Test run can be started after oil filled accordingly.

Table.2

|  | YOXⅡZ 150-320 | YOXⅡZ 360-450 | YOXⅡZ 500-650 | YOXⅡZ 750-1150 |
| --- | --- | --- | --- | --- |
| ＜750r/min | ＜0.5mm | ＜0.6mm | ＜0.7mm | ＜0.8mm |
| ＞750,＜1200r/min | ＜0.4mm | ＜0.5mm | ＜0.6mm | ＜0.7mm |
| ＞1200,＜1500r/min | ＜0.3mm | ＜0.4mm | ＜0.5mm | ＜0.6mm |

Follow this sequence to dismount the coupling:

Release motor screws first then remove motor, then pull out the couplings and brake wheel.

Attention: No mental tools are allowed to beat the Aluminum parts during installation. It is also not allowed to installation by the way of heating.

# Operating Fluid

6.1	 Function of Operating Fluid

The operating fluid is the medium which transmits torque and power from driving wheel to driven wheel. The quantity of fluid affects the transmitted torque directly.

In general, within the specified limits, the more the filling, the higher the torque that can be transmitted.

With constant transmitted torque, the more the filling, the higher the efficiency.

However, the starting torque will also increase and the overload coefficient will

also increase, that is, less overload protection to the driven machine.

Therefore, for any one size of coupling, we can use different filling quantity to meet various requirements of different power and different driven machines.

6.2	 Selection of working fluid

The operating fluid shall has low viscosityμ，high densityγ，high flash point, low pour point, long service life and must be non - corrosive.

We recommend the following values:

Viscosityμ= 32㎜2/s

Densityγ = 0.84~0.86g/㎝3

Flash point ＞ 180℃

Pour point ＜ －10℃

A lot of mineral oil including hydraulic oil, turbine oil, motor oil etc. meet these requirements and can be used, we also recommended # 32 turbine oil.

6.3  Filling Quantity

The quantity of oil filled shall lie within 40% ~ 80% of the total volume, quantity beyond these limits is not allowed, particularly, a coupling must not be fully filled.

For filling above 80%, the rise in temperature during operation or overload will induce excessive internal pressure causing the coupling to leak or even causes serious damages.

For filling below 40%, insufficient lubrication to the bearings will cause higher noise and early failure.

6.4  Sequence of Filling

1.  After the coupling is installed, turn it until the Filler Plug and Fusible Plug are both on the top.

2.  Unscrew Filler Plug and Fusible Plug.

3.  Fill in appropriate amount of oil ( refer to 7.3 “Determination of filling quantity ” ), the oil must pass through a 80 ~ 100 mesh filter, any particle in the oil will cause serious wear to the coupling.

- Screw back and tighten the Fusible Plug.

- Turn the coupling slowly until oil start to flow out from the Filler Hole, measure and record down the height of the centre of Filler Hole to ground. Also mark this height on the motor or protective cover so that the oil level can be easily checked at any time.

- Replace and tighten Filler Plug.

- Special filling device and oil level checking device are required for a coupling mounted in vertical position.

6.5  Checking on Filling Level

The level of oil in the coupling shall be checked regularly to ensure on oil has leaked out. The following sequence shall be followed:

- Turn the coupling until one of the Filler Plug is on the top.

- Unscrew the Filler Plug.

- Turn the coupling slowly until the centre of Filling Hole lies at same level as the mark on motor or protective cover .

- Oil should start to overflow, otherwise, there may be some leakage. Top up to original level with same oil.

- Replace and tighten Filler Plug.

- If step 4 reflects that there may be leakage, run the coupling for some time and check for oil leaking out. The coupling must be repaired if leakage is found.

# Precautions

- Direction of Rotation : The coupling can be used for both directions of  rotation.

- A protective cover must be installed over the coupling.

- The driven machine shall start after the motor has run to speed, if the driven machine doesn’t start, stop the motor immediately. Check whether the machine is blocked or whether there are appropriate amount of oil in the coupling.

- Check the coupling regularly for any leakage. Leakage must be repaired before the coupling is put into use again.

- During continuous operation, the temperature of oil must not exceed 90℃.

- Check the oil after every 3000 hours of operation for ageing, change the oil if necessary. Do not mix different oils.

- Check the Flexible Elements regularly for wear, replace worn Elements.

- Check the alignment of motor shaft and output shaft regularly.

- Never dismantle the coupling unless it is absolutely required. Couplings are dynamically balanced, mark relative position on parts before dismantling. Reassemble of the coupling must. be carried out with utmost care on alignment of parts, fitting of bearings and oil seal rings as well as cleanliness.

- The Fusible Plug protects the coupling from overheated which may lead to serious damages to the coupling and even causes fire hazard. Never replace the Fusible Plug with a blind screw, a Fusible Plug of different response temperature or anything else.

- Special fusible plug is used on the Mechanical Thermal Switch WBQ-II (selected by users with additional cost).

# 8.  Trouble Shooting

  - Driven Machine Cannot Reach Rated Speed

Table.3

| Cause | Action |
| --- | --- |
| 1. Problem with motor or incorrect connection to motor. | Check motor speed, connection and current. |
| 2. Driven machine blocked. | Check for blockage and eliminate. |
| 3. Insufficient oil. | Check oil quantity any refill. |
| 4. Coupling leaks. | Check for leakage, repair and refill oil. |

  - Core of Fusible Plug Melted

Table.4

| Cause | Action |
| --- | --- |
| 1. Insufficient oil. | Check oil quantity any refill. |
| 2. Coupling leaks. | Check for leakage, repair and refill oil. |
| 3. Coupling overloaded. | Check power rating of coupling and driven machine. |
| 4. Driven machine overloaded. | Check loading condition on driven machine. |
| 5. Driven machine blocked. | Check for blockage and eliminate. |
| 6. Frequent starting. | Coupling is heated up on every starting, avoid frequent starting. |
| 7. Frequent or prolong braking of driven machine. | Coupling is heated up on every braking, avoid frequent or prolong braking. |
| 8. Motor remains in Star connection for too long. | Set changeover time for Star / Delta connection to minimum ( 2 - 5 second ). |
| 9. Incorrect Fusible Plug. | Use fusible plug of correct respond temperature. |

8.3	  Excessive Noise or Vibration

Table.5

| Cause | Action |
| --- | --- |
| 1. Excessive misalignment on motor shaft and shaft of driven machine. | Check alignment and correct where necessary. |
| 2. Bearings failed. | Check and replace Bearings, also check that sufficient oil was filled. |
| 3. Loose foundation. | Check and tighten foundation fixing screws, recheck alignment. |
| 4. Worn flexible element. | Replace. |

# 9.  Mechanical Thermal Switch  WBQ-II

Fig . 5: Installation Diagram of Mechanical Thermal Switch WBQ-II

| Item No. | Description | Item No. | Description |
| --- | --- | --- | --- |
| 1 | Standard Fusible Plug | 4 | Limit Switch |
| 2 | Special Fusible Plug | 5 | Bracket |
| 3 | Lever | 6 | Controller |

The Mechanical Thermal Switch WBQ – II is an optional controlling device used to protect the coupling against overheating. Its main difference with the Fusible Plug is that it switches the motor off when response temperature is reached without loss of the working fluid.

Its construction and connection is shown in Fig. 5. It consists of a Special Fusible Plug (2) with a small pin protruding out by about 1 mm. On reaching the response temperature, the pin is released and moves out by 8 to 10 mm. It will then actuate a Limit Switch (4) which sends a signal to the Controller (6) to stop the motor and / or giving an alarm signal.

After the Special Fusible Plug is actuated, the cause for overheating has to be checked and corrected according to section 11.2 Then a new Special Fusible Plug shall be replaced.

Normal response temperature of the WBQ-II is 110±5℃, a standard Fusible Plug of response temperature of 140℃ must also be used as a device for double safety.

The WBQ-II shall be installed according to Fig. 5

Fig.6  Electrical schematics

Fig.7 Special Fusible Plug

The WBQ-II is not suitable for use on Turbo Wheel Drive installation.

# 10. Repair

No special maintenance is needed during the operation of fluid couplings if users follow this manual. If couplings is failed, please contact us to analyze the possible reasons. Send the couplings back to our company for repair.

# 11. Wear-out parts

The wear-out parts lists will be provided according to the different size of couplings on delivery.

# 12.  Spare Parts and Service

On every coupling you will find its Serial Number Stamped on the aluminum Shell. In case you need any spare part or service, please inform us the Type of the coupling, its Serial Number and the Part number and Part description ( refer to Fig.1).

# Text boxes

(n)

speed

Input

concentricity

&

Parallelism

type

&

Size