## Contents

| Preface | 1 |
| --- | --- |
| Safety | 2 |
| Construction | 3 |
| Operation Principle | 4 |
| Specification | 5 |
| Performance Parameters | 6 |
| Installation | 9 |
| Operating Fluid | 11 |
| 9. Filling and Filling Control | 12 |
| Precautions | 14 |
| 11. Trouble Shooting | 15 |
| 12. Mechanical Thermal Switch | 16 |
| 13. Spare parts and Service | 18 |

- Preface

This manual will help you to use our coupling in a safe, proper and economical way.

This manual shall always be read and used by every person before working on the coupling, it shall be available on the machine site for easy reference.

The coupling is manufactured to the state of art and approved safety regulations. Nevertheless, proper installation, maintenance and handling is indispensable for the coupling to provide best performance and service life as well as to safeguard the safety of operating personnel.

The coupling is designed to transmit power at rated values and under definite conditions. Incorrect use including incorrect installation or filling, use for other purpose or excessive power or speed etc., will cause damages to the coupling and other machines and may even endanger the safety of operating personnel. The manufacturer is not liable for any responsibility on all losses out of incorrect handling of the coupling.

This manual has been issued with utmost care. However, in case you need any further information, please contact

Guangdong Zhongxing Power Transmission Co., Ltd.

45 Hedi Road, Ducheng town, Yunan County 527100

Guangdong Province

P.R.China

Tel:  ( 0766 ) 7592180 , 7331005，7596083

Fax:  (0766 ) 7596216, 7597178

Guangzhou Office: 	Xiatiang West Road, Guangzhou

Telephone: ( 86 20 )86599392

Fax:	   ( 86 20 ) 86599384

Beijing Office:		Tele/Fax:  ( 86 10 ) 64934623

Shanghai Office:	Tele/Fax:  ( 86 21 ) 56056555

- Safety

2.1 General        Always follow instructions in this manual, incorrect handling of the coupling will lead to damages and even fatal injury!

2.2 Lifting         Make sure the lifting device has sufficient loading capacity for the coupling and check that it is in sound condition.

2.3 Mounting      Coupling must be mounted securely and a protective cover must be installed. In no case shall the coupling be started without a protective cover.

2.4 Filling Oil     Only recommended filling oil shall be used, improper filling oil may

affect performance

cause corrosion to the coupling

cause irritation when contact with skin

cause fire hazard

2.5 Handling of Oil Some of the oils are caustic, irritating or harmful. Put on protective gloves and wear glasses when handling them. Wash hands carefully after the work is finished.

2.6 Filling Control  Follow recommended filling level.

The coupling must never be filled to over 80% of its internal volume, otherwise the excessive internal pressure produced by heating may cause serious damages to the coupling and may even lead to fatal injury!

2.7 Fusible Plug    The Fusible Plug protects the coupling from overheated which may lead to serious damages to the coupling and even causes fire hazard. Never replace the Fusible Plug with a screw, a Fusible Plug of different response temperature or anything else.

2.8 Maintenance   Power must be switched off before any maintenance work is carried out. Lock shall be used to avoid unauthorised switch on. Replace the protective cover before switch on power.

- Construction

（附YOXvnz结构图）

Fig 1-1

1. Brake wheel   2.Quincoucial flexible element        3.Half connection coupling    4.Longer delay chamber  5.Oil seal  6.Hub  7. Bearing  8. Pumpwheel   9. Filler Plug    10. Turbo wheel  11. Shell  12. Fusible Plug   13. Whorled ring   14. Bearing   15. Cover  16. Oil seal

（附YOXvsnz结构图）

Fig 1-2

1. Brake wheel   2.Quincoucial flexible element       3.Half connection coupling    4.Longer delay chamber  5.Oil seal  6.Hub  7. Bearing  8. Pumpwheel   9. Filler Plug    10. Turbo wheel  11. Aux chamber(Shell)  12. Fusible Plug   13. Whorled ring   14. Bearing   15. Cover  16. Oil seal

（附YOXvⅡz结构图）

Fig 1-3

1. Holding disc   2. .Longer delay chamber   3.Oil seal    4.Bearing  5. Filler Plug  6. Pumpwheel  7. Turbo wheel  8.Shell  9. Fusible Plug   10. Whorled ring   11. Hub  12.Bearing   13. Oil seal   14.Connection shaft  15. Flexible element   16. Brake wheel

（附YOXvsⅡz结构图）

Fig 1-4

1. Holding disc   2. .Longer delay chamber   3.Oil seal    4.Bearing  5. Filler Plug  6. Pumpwheel  7. Turbo wheel  8.Aux chamber  9. Whorled ring   10. Fusible plug  11. Hub  12.Bearing   13. Oil seal   14.Connection shaft  15/ Bearing stand  16. Flexible element   17. Brake wheel

- Operation Principle

The Fluid Coupling is a hydrodynamic coupling based on Foettinger’s principle. Its main components are two bladed wheels-an Outer Wheel and an Inner Wheel, the space between them is partially filled by an operating fluid, usually oil.

In most applications, the Outer Wheel is driven by input motor, the rotating wheel brings the fluid into rotation and thus converts the input mechanical energy into potential and kinetic energy of the fluid. The rotating fluid then drives the Inner Wheel into rotation and therefore converts the energy back into mechanical energy through the Inner Wheel and Coupling Hub to the driven machine.

In this way, the motor is started at very small load regardless of the heavy driven masses. So the motor can run up very quickly and be protected against heavy starting current. For YOXvnz，YOXvsnz series, matched motor can be chosen as per 1.5-1.8 times of rated load of couplings, and for YOXvⅡz，YOXvsⅡz series, matched motor can be chosen as per 1.1-1.35 times of rated load of couplings

The driven machine is then started slowly. The slow and smooth acceleration on driven machine also protects the driven machine from excessive torque to prolong its service life.

The Fusible Plug is a device to protect the coupling against overheating. If the output of the coupling is braked or blocked, the input power will completely turns into heat in heating up the working fluid. If the problem is not remedied within certain time, the working fluid will reach the response temperature of the Fusible Plug, the core of it will melt and the working fluid will escape through this opening and thus separates the input and output drives. This can prevent the working fluid from getting too hot and causes serious damages or even fire hazard. Never replace a Fusible Plug with any other screw.

In some special cases, the coupling can be installed in the opposite direction, i.e. the motor drives the Inner Wheel which then transmits the energy to the Outer Wheel and then to the driven machine.This is called Inner Wheel Drive while the most usual arrangement of Outer Wheel driving Inner Wheel is called Outer Wheel Drive. Both arrangements can transmit energy but will have slightly different performance characteristics.

- Main connection dimensions and tech. parameter

  - Main cnnection dimensions and tech. parameter

5.1.1. All dimensions of bores, keyways in table 1, 2, 3 and 4 can be made as per user request on condition that data provied falls within the limit in the tables.

5.1.2. For any specific connection requirement, please state accordingly and order will be received and made in due case.

5.1.3. User shall provide related data about outline dimensions and its construction.

Table 1． Connection dimensions and tech. parameter for YOXvnz series.

| Size | Input Speed n(rpm) | Rated power N(kw) | Overload Coeff. Tg | Efficiency η | Diameter Fig. 1 D(mm) | Length Fig. 1 A(mm) | A1 (mm) | A2 (mm) | Input Bore and Length Max. | Output Bore and Length Max. | Brake wheel dimension(mm | Max. Filling qmin(l) | Min. Filling qmax(l) | Weight (kg) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Starting | Braked |  |  |  |  |  | d1/L1(mm) | d2/L(mm) | d3 | d4 | B | 40% | 80% |  |
| YOXvsnz360 | 1000 1500 | 5-10 16-30 | 1.5-1.8 | 2-2.5 | 0.96 | φ428 | 331 | 278 | 10 | φ55 110 | φ60 110 | Prepare according to user’s reqirement | 3.8 | 9.8 | 45 |
| YOXvsnz400 | 1000 1500 | 8-18.5 28-48 |  |  |  | φ472 | 368 | 308 | 10 | φ60 120 | φ70 140 |  | 5.8 | 10.4 | 68 |
| YOXvsnz450 | 1000 1500 | 15-30 50-90 |  |  |  | φ530 | 419 | 353 | 10 | φ70 140 | φ75 140 |  | 8.3 | 15 | 85.5 |
| YOXvsnz500 | 1000 1500 | 25-50 68-144 |  |  |  | φ582 | 462 | 391 | 15 | φ90 170 | φ90 170 |  | 11.4 | 20.6 | 116 |
| YOXvsnz560 | 1000 1500 | 40-80 120-270 |  |  |  | φ634 | 508 | 433 | 15 | φ100 210 | φ100 210 |  | 14.6 | 26.4 | 138 |
| YOXvsnz600 | 1000 1500 | 60-115 200-360 |  |  |  | φ695 | 550 | 467 | 15 | φ100 210 | φ100 210 |  | 18.6 | 33.6 | 180 |
| YOXvsnz650 | 1000 1500 | 90-176 260-480 |  |  |  | φ760 | 605 | 520 | 15 | φ130 210 | φ130 210 |  | 26.6 | 48 | 237 |
| YOXvsnz750 | 1000 1500 | 170-330 380-760 |  |  |  | φ860 | 648 | 550 | 20 | φ150 250 | φ140 250 |  | 37.7 | 68 | 394 |
| YOXvsnz875 | 1000 1500 | 140-280 330-620 |  |  |  | φ992 | 738 | 632 | 20 | φ150 250 | φ150 250 |  | 62.1 | 112 | 546 |

Table 2． Connection dimensions and tech. parameter for YOXvsnz series.

| Size | Input Speed n(rpm) | Rated power N(kw) | Overload Coeff. Tg | Efficiency η | Diameter Fig. 1 D(mm) | Length Fig. 1 A(mm) | A1 (mm) | A2 (mm) | Input Bore and Length Max. | Output Bore and Length Max. | Brake wheel dimension(mm | Max. Filling qmin(l) | Min. Filling qmax(l) | Weight (kg) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Starting | Braked |  |  |  |  |  | d1/L1(mm) | d2/L(mm) | d3 | d4 | B | 40% | 80% |  |
| YOXvsnz360 | 1000 1500 | 5-10 16-30 | 1.5-1.8 | 2-2.5 | 0.96 | φ428 | 331 | 278 | 10 | φ55 110 | φ60 110 | Prepare according to user’s reqirement | 5.5 | 8.8 | 50 |
| YOXvsnz400 | 1000 1500 | 8-18.5 28-48 |  |  |  | φ472 | 368 | 308 | 10 | φ60 120 | φ70 140 |  | 7.7 | 13.5 | 74 |
| YOXvsnz450 | 1000 1500 | 15-30 50-90 |  |  |  | φ530 | 419 | 353 | 10 | φ70 140 | φ75 140 |  | 11.1 | 19.5 | 93.5 |
| YOXvsnz500 | 1000 1500 | 25-50 68-144 |  |  |  | φ582 | 462 | 391 | 15 | φ90 170 | φ90 170 |  | 15.3 | 26.8 | 134 |
| YOXvsnz560 | 1000 1500 | 40-80 120-270 |  |  |  | φ634 | 508 | 433 | 15 | φ100 210 | φ100 210 |  | 19.5 | 34.2 | 159 |
| YOXvsnz600 | 1000 1500 | 60-115 200-360 |  |  |  | φ695 | 550 | 467 | 15 | φ100 210 | φ100 210 |  | 24.9 | 43.6 | 200 |
| YOXvsnz650 | 1000 1500 | 90-176 260-480 |  |  |  | φ760 | 605 | 520 | 15 | φ130 210 | φ130 210 |  | 35.6 | 62.4 | 257 |
| YOXvsnz750 | 1000 1500 | 170-330 380-760 |  |  |  | φ860 | 648 | 550 | 20 | φ150 250 | φ140 250 |  | 50.5 | 88.4 | 425 |
| YOXvsnz875 | 1000 1500 | 140-280 330-620 |  |  |  | φ992 | 738 | 632 | 20 | φ150 250 | φ150 250 |  | 83.1 | 146 | 596 |

Table 3． Connection dimensions and tech. parameter for YOXvⅡz series.

| Size | Input Speed n(rpm) | Rated power N(kw) | Overload ratio Tg | Effi.η d1/L1 (mm) | Input Bore and Length Max. d1/L1(mm) | Output Bore and Length Max. d2/L2 | Filling qty（l） | Dimensions（mm） | Weight kg |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Started | Brated |  |  |  | 40% qmin | 80% qmin | A | A1 | D | B | D1 | A4 | C | E |  |
| YOXVIIZ400 | 1000 | 8-18.5 | 1.35-1.5 | 2-2.3 | 0.96 | φ65/140 | φ65/140 | 5.8 | 10.4 | 556 | 358 | φ472 | 150 | φ315 | 10 | 38 | 50 | 116 |
|  | 1500 | 28-48 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVIIZ450 | 1000 | 15-30 |  |  |  | φ75/140 | φ75/140 | 8.3 | 15 | 581 | 383 | φ530 | 150 | φ315 | 10 | 38 | 30 | 132 |
|  | 1500 | 50-90 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVIIZ500 | 1000 | 25-50 |  |  |  | φ90/170 | φ90/170 | 11.4 | 20.6 | 672 | 431 | φ582 | 190 | φ400 | 10 | 41 | 40 | 165 |
|  | 1500 | 68-144 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVIIZ560 | 1000 | 40-80 |  |  |  | φ110/210 | φ100/210 | 14.6 | 26.4 | 748 | 503 | φ634 | 190 | φ400 | 10 | 45 | 70 | 210 |
|  | 1500 | 120-270 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVIIZ600 | 1000 | 60-115 |  |  |  | φ110/210 | φ110/210 | 18.6 | 33.6 | 787 | 517 | φ695 | 210 | φ500 | 15 | 45 | 50 | 350 |
|  | 1500 | 200-360 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVIIZ650 | 1000 | 90-176 |  |  |  | φ120/210 | φ120/210 | 26.6 | 48 | 825 | 555 | φ760 | 210 | φ500 | 15 | 45 | 35 | 390 |
|  | 1500 | 260-480 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVIIZ750 | 1000 | 170-330 |  |  |  | φ130/210 | φ130/210 | 37.7 | 68 | 920 | 590 | φ860 | 265 | φ630 | 15 | 50 | 40 | 513 |
|  | 1500 | 380-760 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVIIZ875 | 750 | 140-280 |  |  |  | φ140/250 | φ140/250 | 62.1 | 112 | 1032 | 672 | φ992 | 265 | φ630 | 20 | 75 | 40 | 690 |
|  | 1000 | 330-620 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Table 4． Connection dimensions and tech. parameter for YOXvsⅡz series.

| Size | Input Speed n(rpm) | Rated power N(kw) | Overload ratio Tg | Effi.η d1/L1 (mm) | Input Bore and Length Max. d1/L1(mm) | Output Bore and Length Max. d2/L2 | Filling qty（l） | Dimensions（mm） | Weight kg |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Started | Brated |  |  |  | 40% qmin | 80% qmin | A | A1 | D | B | D1 | A4 | C | E |  |
| YOXVSIIZ400 | 1000 | 8-18.5 | 1.1-1.35 | 2-2.3 | 0.96 | φ65/140 | φ65/140 | 7.7 | 15.3 | 556 | 358 | φ472 | 150 | φ315 | 10 | 38 | 50 | 120 |
|  | 1500 | 28-48 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVSIIZ450 | 1000 | 15-30 |  |  |  | φ75/140 | φ75/140 | 11.1 | 19.5 | 581 | 383 | φ530 | 150 | φ315 | 10 | 38 | 30 | 135 |
|  | 1500 | 50-90 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVSIIZ500 | 1000 | 25-50 |  |  |  | φ90/170 | φ90/170 | 15.3 | 26.8 | 672 | 431 | φ582 | 190 | φ400 | 10 | 41 | 40 | 183 |
|  | 1500 | 68-144 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVSIIZ560 | 1000 | 40-80 |  |  |  | φ110/210 | φ100/210 | 19.5 | 34.2 | 748 | 503 | φ634 | 190 | φ400 | 10 | 45 | 70 | 240 |
|  | 1500 | 120-270 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVSIIZ600 | 1000 | 60-115 |  |  |  | φ110/210 | φ110/210 | 24.9 | 43.6 | 787 | 517 | φ695 | 210 | φ500 | 15 | 45 | 50 | 350 |
|  | 1500 | 200-360 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVSIIZ650 | 1000 | 90-176 |  |  |  | φ120/210 | φ120/210 | 35.6 | 62.4 | 825 | 555 | φ760 | 210 | φ500 | 15 | 45 | 35 | 390 |
|  | 1500 | 260-480 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVSIIZ750 | 1000 | 170-330 |  |  |  | φ130/210 | φ130/210 | 50.5 | 88.4 | 920 | 590 | φ860 | 265 | φ630 | 15 | 50 | 40 | 513 |
|  | 1500 | 380-760 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| YOXVSIIZ875 | 750 | 140-280 |  |  |  | φ140/250 | φ140/250 | 83.1 | 145.6 | 1032 | 672 | φ992 | 265 | φ630 | 20 | 75 | 40 | 690 |
|  | 1000 | 330-620 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

5.2 Calculation of Torque and Power

Characteristic CurvesλB=f(i) (see Fig3, 4, 5, 6, 7, 8, 9, 10 and 11)

The following formulae can be used to calculate the Transmitted Torque and Transmitted Power at different input speed nB

M = λB·γ·nB2·D5

N = 1/975·λB·γ·nB3·D5

where:   M  -  Transmitted Torque (kg.m)

γ  -  Density of fluid (for #32 turbine oilγ= 860kg/m3)

nB   -  Input speed (rpm)

λB  -  Performance Figure (min2/m). It can be obtain from Fig. provided.

D  -  Effective Diameter of Wheel (m)

N  -  Transmitted Power (kw)

5.3 Relation curve of Power transmitted and filling quantity: N= f (qc)

The filling quantity depends on

5.3.1. Transmitted Power N

5.3.2. Input Speed nB

5.3.3. Slip at rated torque (Slip = 1 – efficiencyη)

User shall follow the recommended filling quantity when it is provided.

User may also obtain the filling volume from Fig. 3, but it can only be used as a guide for trial. And depending on the trial result, filling level shall be adjusted to meet actual power transmitted by:

- Increase filling quantity if transmitted torque is not enough or

- Reduce filling quantity if transmitted torque is too high

However, the filling quantity can never exceed the maximum value nor less than the minimum value , which is from 40% to 80% .

qc=q/Q,

where:

qc – oil filling rate

q – actual filling quantity

Q – general filling quantity (can be reviewed in tech. parameter table)

Relation curve of Power transmitted and filling quantity will be delivered together with hydraulic couplings.

Fig 12 Relation curve of Power transmitted and filling quantity of YOXvnz875(附图)

Fig.2 Characteristic Curves for YOXvsnz650 Couplings and Fig 3-6 general Characteristic Curves for YOXvs series

Filling Quantity:80%, 70%, 62.5%, 55% and 50%

Working Fluid: #32 Turbine oil,Density γ=830 kg/m3

Operating Temperature:70°C~80°C

（YOXvsnz650及YOXvs系列原始特性曲线-Fig2-Fig3,4,5,6)

- Installation

Fig 13 YOXvsnz and YOXvnz installing dwg

- Brake wheel  2.Dial calibrater  3.Shelf for dial calibrater  4.Feeler  5.half connection coupling  6.Mounting spindle, bead flange and pin

Fig14 YOXvsⅡz和YOXvⅡz installing dwg

1. Dial calibrater   2. Connecting shaft   3. Braked wheel

The coupling is installed

- In case of outer wheel drive (YOXvⅡz and YOXvsⅡnz)

- by mounting it on the input shaft of the driven machine

- connected to the motor via a flexible coupling

- In case of inner wheel drive (YOXvsnz and YOXvnz)

- by mounting it on the motor shaft

- connected to the input shaft of driven machine via a flexible coupling

For most applications, the coupling shall be used as outer wheel drive which gives a better performance.

Couplings shall only be installed as they are designed for.

Follow this sequence to install the coupling:

- Slightly fasten bolts on the motor, check alignment of input shaft and output shaft with dial gauge, place shims under the motor bracket to correct alignment, make sure that they fall within the following admissible values

Table 5

| Spec. Allowed | YOXvsnz360-450 YOXvnz360-450 YOXvsⅡz360-450 YOXvⅡz360-450 | YOXvsnz500-650 YOXvnz500-650 YOXvsⅡz500-650 YOXvⅡz500-650 | YOXvsnz750-1150 YOXvnz750-1150 YOXvsⅡz750-1150 YOXvⅡz750-1150 |
| --- | --- | --- | --- |
| <750r/min | <0.6mm | <0.8mm | <0.8mm |
| <750<1200r/min | <0.5mm | <0.6mm | <0.7mm |
| <1200<1500r/min | <0.4mm | <0.5mm | <0.6mm |

2  Fit suitable keys on the shafts of motor and driven machine, apply a suitable lubricant

3  Fix the coupling on the shaft of motor.

4. There shall be a screw at the motor shaft end to avoid vibration. In case of shaft-end fixing, please fix Mounting spindle in Fig 13 onto motor shaft.

5. Fix Brake wheel on the high-speed shaft of reducer; and make Quincoucial flexible element fall in with the gear of Brake wheel

6.Make motor together with coupling interlocked with Brake wheel and check end clearance.

7.Fix the bolts of motor and working machine, and recheck radial misalignment of motor and working machine shaft. As per to installation diagram: Fix the dial calibrater(3) onto half coupling and turn the brake wheel and check the value until it is acceptable; then fix the bolts of motor and reducer.

8. Fill oil according to oil filling curve and start operation.

For disassembly, release the bolts of motor stand to remove motor, then disassembly the coupling.

During installation process, do not hit the preface of aluminium casting, and no heating shall be proceeded

- Operating Fluid

8.1  Function of Operating Fluid

The operating fluid is the medium which transmits torque and power from driving wheel to driven wheel. The quantity of fluid affects the transmitted torque directly.

In general, within the specifled limits, the more the filling, the higher the torque that can be transmitted.

With constant transmitted torque, the more the filling, the higher the efficiency.

However, the starting torque will also increase and the overload coefficient will

also increase, that is, less overload protection to the driven machine.

Therefore, for any one size of coupling, we can use different filling quantity to meet various requirements of different power and different driven machines.

8.2  Selection of working fluid

The operating fluid shall has low viscosityμ，high densityγ，high flash point, low pour point, long service life and must be non - corrosive.

We recommend the following values:

Viscosityμ= 32㎜2/s

Densityγ = 0.84~0.86g/㎝3

Flash point ＞ 180℃

Pour point ＜ －10℃

A lot of mineral oil including hydraulic oil, turbine oil, motor oil etc. meet these requirements and can be used, we also recommend # 32 turbine oil.

- Filling and Filling Control

9.1  Filling Quantity

The quantity of oil filled shall lie within 40% ~ 80% of the total volume, quantity beyond these limits is not allowed, particularly, a coupling must not be fully filled.

For filling above 80%, the rise in temperature during operation or overload will induce excessive internal pressure causing the coupling to leak or even causes serious damages.

For filling below 40%, insufficient lubrication to the bearings will cause higher noise and early failure.

9.2  Sequence of Filling

1.  After the coupling is installed, turn it until the Filler Plug and Fusible Plug are both on the top.

2.  Unscrew Filler Plug and Fusible Plug.

3.  Fill in appropriate amount of oil ( refer to 6.2 “Determination of filling quantity ” ), the oil must pass through a 80 ~ 100 mesh filter, any particle in the oil will cause serious wear to the coupling.

- Screw back and tighten the Fusible Plug.

- Turn the coupling slowly until oil start to flow out from the Filler Hole, measure and record down the height of the centre of Filler Hole to ground. Also mark this height on the motor or protective cover so that the oil level can be easily checked at any time.

- Replace and tighten Filler Plug.

- Special filling device and oil level checking device are required for a coupling mounted in vertical position.

9.3  Checking on Filling Level

The level of oil in the coupling shall be checked regularly to ensure on oil has leaked out. The following sequence shall be followed:

- Turn the coupling until one of the Filler Plug is on the top.

- Unscrew the Filler Plug.

- Turn the coupling slowly until the centre of Filling Hole lies at same level as the mark on motor or protective cover made in above section 9.2 step 5.

- Oil should start to overflow, otherwise, there may be some leakage. Top up to original level with same oil.

- Replace and tighten Filler Plug.

- If step 4 reflects that there may be leakage, run the coupling for some time and check for oil leaking out. The coupling must be repaired if leakage is found.

- Precautions

- Direction of Rotation : The coupling can be used for both directions of  rotation.

- A protective cover must be installed over the coupling.

- The driven machine shall start after the motor has run to speed, if the driven machine doesn’t start, stop the motor immediately. Check whether the machine is blocked or whether there are appropriate amount of oil in the coupling.

- Check the coupling regularly for any leakage. Leakage must be repaired before the coupling is put into use again.

- During continuous operation, the temperature of oil must not exceed 90℃.

- Check the oil after every 3000 hours of operation for aging, change the oil if necessary. Do not mix different oils.

- Check the Flexible Elements regularly for wear, replace worn Elements.

- Check the alignment of motor shaft and output shaft regularly.

- Never dismantle the coupling unless it is absolutely required. Couplings are dynamically balanced, mark relative position on parts before dismantling. Reassemble of the coupling must. be carried out with utmost care on alignment of parts, fitting of bearings and oil seal rings as well as cleanliness.

- The Fusible Plug protects the coupling from overheated which may lead to serious damages to the coupling and even causes fire hazard. Never replace the Fusible Plug with a blind screw, a Fusible Plug of different response temperature or anything else.

- A Star / Delta connection to the motor is not required unless for a weak power supply. In this case, set the changeover time from Star to Delta as short as possible ( 2 to 5 seconds ).

11.  Trouble Shooting

11.1   Driven Machine Cannot Reach Rated Speed

| Cause | Action |
| --- | --- |
| 1. Problem with motor or incorrect connection to motor. | Check motor speed, connection and current. |
| 2. Driven machine blocked. | Check for blockage and eliminate. |
| 3. Insufficient oil. | Check oil quantity any refill. |
| 4. Coupling leaks. | Check for leakage, repair and refill oil. |

11.2   Core of Fusible Plug Melted

| Cause | Action |
| --- | --- |
| 1. Insufficient oil. | Check oil quantity any refill. |
| 2. Coupling leaks. | Check for leakage, repair and refill oil. |
| 3. Coupling overloaded. | Check power rating of coupling and driven machine. |
| 4. Driven machine overloaded. | Check loading condition on driven machine. |
| 5. Driven machine blocked. | Check for blockage and eliminate. |
| 6. Frequent starting. | Coupling is heated up on every starting, avoid frequent starting. |
| 7. Frequent or prolong braking of driven machine. | Coupling is heated up on every braking, avoid frequent or prolong braking. |
| 8. Motor remains in Star connection for too long. | Set changeover time for Star / Delta connection to minimum ( 2 - 5 second ). |
| 9. Incorrect Fusible Plug. | Use fusible plug of correct respond temperature. |

11.3   Excessive Noise or Vibration

| Cause | Action |
| --- | --- |
| 1. Excessive misalignment on motor shaft and shaft of driven machine. | Check alignment and correct where necessary. |
| 2. Bearings failed. | Check and replace Bearings, also check that sufficient oil was filled. |
| 3. Loose foundation. | Check and tighten foundation fixing screws, recheck alignment. |
| 4. Worn flexible element. | Replace. |

12.  Mechanical Thermal Switch  WBQ-II

Fig . 8 : Installation Diagram of Mechanical Thermal Switch WBQ-II

（WBQ-II装置安装图）

Fig 8

| Item No. | Description | Item No. | Description |
| --- | --- | --- | --- |
| 1 | Standard Fusible Plug | 4 | Limit Switch |
| 2 | Special Fusible Plug | 5 | Bracket |
| 3 | Lever | 6 | Alarm device |
| 7 | Alarm light(red) | 8 | Work light(green) |
| 9 | Fuse |  |  |

(WBQ-II断电机构接线示意图)

LK1- Normally closed contact for Limit Switch

LK2- Normally open contact for Limit Switch

The Mechanical Thermal Switch WBQ – II is an optional controling device used to protect the coupling against overheating. Its main difference with the Fusible Plug is that it switches the motor off when response temperature is reached without loss of the working fluid.

Its construction and connection is shown in Fig. 8. It consists of a Special Fusible Plug (2) with a small pin protruding out by about 1 mm. On reaching the response temperature, the pin is released and moves out by 8 to 10 mm. It will then actuate a Limit Switch (4) which sends a signal to the Alarm device (6) to stop the motor and / or giving an alarm signal.

After the Special Fusible Plug is actuated, the cause for overheating has to be checked and corrected according to section 11.2 Then a new Special Fusible Plug shall be replaced.

Normal response temperature of the WBQ-II is 110±5℃, a standard Fusible Plug of response temperature of 140℃ must also be used as a device for double safety.

The WBQ-II shall be installed according to Fig. 8.

13.  Spare Parts and Service

On every coupling you will find its Serial Number Stamped on the aluminium Shell. In case you need any spare part or service, please inform us the Type of the coupling, its Serial Number and the Part number and Part description ( refer to Fig. 1 ) at

Guangdong  Zhongxing  Power  Transmission  Co.Ltd.

45 Hedi Road, Ducheng town, Yunan County 527100

Guangdong Province

P.R.China

Tel：（0766）7592180  7596083  7331005

7333167（Tech. Dep.） 7331352（Pro. Dep.）

Fax：（0766）7596216  7597178

http://www.gdzxpt.com

# Text boxes

n

Input speed

ment

align

mis